## Slide 1: Lesion 7 Advance pattern operation LAB 06 (Wheel)
IDE 33101CAID Dr. Palang WONGTANASUPORN lecture 10-11
17” Rim
Step by step
reveal

## Slide 2: Preparation
Your own design wheel
Standard size of a blank rim
Standard size and position of connector and nuts

## Slide 3: Rim body
Set sketch view as xy plane
Use X axis as rotation axis
Draw cross-section of rim
Turn on Revolve operation
Revolve profile 360 degree

## Slide 4: Front plate
Use XZ plane as working plane
Create profile sketch for revolve
Make sure the rotation axis is the same with rim ( x axis)

## Slide 5: Revolving front plate
Turn on revolve operation
Select cross section as profile
Rotate 360 degree

## Slide 6: Pattern sketch
Create a work plane over YZ plane
Sketch a main pattern for cut off the front plate
Make sure the sketch will complete the close loop of circle after circular pattern operation

## Slide 7: Make extrude part for circular pattern
Turn on extrude operation
Select close loop section as profile
Extrude (intersect)
Click OK

## Slide 8: Redefine extruded part
The extruded part need to be redefine
Modify operation such as Chamfer Fillet Draft may be concerned

## Slide 9
Turn on Circular pattern operation
Select extruded part as solid
Set placement as 4 at 360 degree
Click OK

## Slide 10: Socket rod
Create socket rod for screw shaft and bold spacer
You need to make position for a hold then create socket rod by using revolve operation

## Slide 11: Hold Pattern
Use circular pattern to arrange other socket rod

## Slide 12: Redefine the front plate
Redefine the front plate especially the sharp edges after pattern operation and also reduce unnecessary part

## Slide 13: Assembly
Combine front plate and rim
Redefine the sharp edges after combined